## Slide 1: CH2PH2: Chemical Kinetics
Dr. James Hallett
j.e.hallett@reading.ac.uk

## Slide 2: Lecture 5
CH2PH2: Chemical Kinetics

## Slide 3: experimental reaction kinetics

## Slide 4: Studying reaction kinetics
We typically need:
Analytical techniques to measure the reaction
Some method to mix our sample effectively
We could use some other method to initiate the reaction in situ
Need to think about the timescale of the reaction and analytical method

## Slide 5: Analytical techniques for kinetics measurements
Time
Fast
Slow
Optical Spectroscopy
Mass Spectroscopy
NMR
Titration
Optimise sample preparation to suit technique of choice
Notes: Fast and slow methods e.g. absorbance as a function of t, spectra, versus titration, mass spec, NMR

## Slide 6: Experimental Approaches
Real-time
Quenching
Continuous flow
Stopped flow

## Slide 7: Real-time monitoring
Measure something in the reaction vessel as the reaction takes place
Timescale depends on analytical technique and the speed of mixing
Analytical technique must be fast compared to reaction and non-destructive

## Slide 8: Real-time monitoring
Advantages
Doesn’t necessarily need special equipment
Disadvantages
Containers might need to be specially designed

## Slide 9: Real-time monitoring: X-ray scattering of gold nanoparticle synthesis
Koerner, H., MacCuspie, R. I., Park, K., & Vaia, R. A. (2012). In situ UV/Vis, SAXS, and TEM study of single-phase gold nanoparticle growth. Chemistry of Materials, 24(6), 981-995.
Background context

## Slide 10: In-situ monitoring – in practice
Hayward, D. W., Chiappisi, L., Prévost, S., Schweins, R., & Gradzielski, M. (2018). A small-angle neutron scattering environment for in-situ observation of chemical processes. Scientific reports, 8(1), 1-11.
Background context

## Slide 11: In-situ monitoring – in practice
pD
Background context

## Slide 12: Quenching
Reaction (or an aliquot) is “quenched” after a certain amount of time (≥ ms).
Quenching can be carried out by mixing, eg, sudden change in pH or dilution, or by a sudden drop in temperature.
Have to be sure that quenching is fast compared to the reaction and does not cause any other changes

## Slide 13: Quenching
Advantages
Analytical approaches can be slow and/or destructive
Quenched samples can be stored and reanalysed using different methods
Disadvantages
Timescale limited by speed of quenching

## Slide 14: Quenching: gold-citrate aggregates in gold nanoparticle synthesis
1 min.
4 min.
20 min.
120 min.
Doyen, M., Bartik, K., & Bruylants, G. (2013). UV–Vis and NMR study of the formation of gold nanoparticles by citrate reduction: Observation of gold–citrate aggregates. Journal of colloid and interface science, 399, 1-5.
Background context
Notes: Ice bath quench

## Slide 15: Continuous flow
Observing the composition at different positions = reaction mixtures at different times after mixing.
Timescale ≥ ms
Analytical technique must be position specific
Analytical technique can be slow compared to reaction

## Slide 16: Continuous flow
Advantages
Conceptually simple
Fast mixing
Disadvantages
Large volumes of reagents required
Requires movable spectrometer

## Slide 17: Continuous flow
Advantages
Conceptually simple
Fast mixing
Disadvantages
Large volumes of reagents required
Requires movable spectrometer

## Slide 18
Jang, H., Pawate, A. S., Bhargava, R., & Kenis, P. J. (2019). Polymeric microfluidic continuous flow mixer combined with hyperspectral FT-IR imaging for studying rapid biomolecular events. Lab on a Chip, 19(15), 2598-2609.
https://www.youtube.com/watch?v=_V-iSOOTBAs
Microfluidic FT-IR Imaging
Background context

## Slide 19
Jang, H., Pawate, A. S., Bhargava, R., & Kenis, P. J. (2019). Polymeric microfluidic continuous flow mixer combined with hyperspectral FT-IR imaging for studying rapid biomolecular events. Lab on a Chip, 19(15), 2598-2609.
Microfluidic FT-IR Imaging
Background context

## Slide 20: Stopped flow
Fast mixing can be achieved in ~1ms with “stopped flow” technique (so appropriate if reaction is slower than this)
Monitoring
This can be used with liquids or gases.
(Picture from Atkins’ Physical Chemistry 7th ed)

## Slide 21: Stopped flow
Advantages
Uses small sample volumes – particularly beneficial if your reagent is expensive/hard to produce
Disadvantages
Requires specialist kit

## Slide 22: CRISPR DNA Editing
Raper, A. T., Stephenson, A. A., & Suo, Z. (2018). Functional insights revealed by the kinetic mechanism of CRISPR/Cas9. Journal of the American Chemical Society, 140(8), 2971-2984.
Background context

## Slide 23: CRISPR DNA Editing
Raper, A. T., Stephenson, A. A., & Suo, Z. (2018). Functional insights revealed by the kinetic mechanism of CRISPR/Cas9. Journal of the American Chemical Society, 140(8), 2971-2984.
Jennifer Doudna and Emmanuelle Charpentier – Nobel Prize in Chemistry 2020
Background context

## Slide 24: ULTRAfast reactions
CH2PH2 Chemical Kinetics

## Slide 25: Reaction time << ms?

## Slide 26: Starting reactions with light
Before first lasers invented (1960s), light flashes could be generated in microseconds (10-6 s)
“Flash photolysis” – developed by Norrish and Porter in the 1950s – use a flash of light to break bonds, to produce reactive species (“pump” pulse)
Monitor reaction spectroscopically with another beam (“probe”) in real time.
Nowadays, lasers can easily generate nanosecond (10-9 s) to femtosecond (10-15 s) pulses

## Slide 27: Photolysis of Acetone to produce methyl radicals
C
O
CH3
CH3
·CH3
·C
O
CH3
·CH3+CO
fast
pump
2 ·CH3
C2H6
probe
“Pump” pulse can
  Break bonds to give radicals
  Generate electronically excited states
  Remove a (designed light-sensitive) protecting group from, e.g., an enzyme
  Produce a precursor which (quickly) produces reagent
  Heat; by (a) mixing a dye that absorbs at a certain wavelength, or(b) using an IR pulse tuned to, eg, OH stretch in water.

## Slide 28: Designing a pump-probe experiment
Pump beam is intense (to cause chemical change)
Probe beam is not intense (this should not cause chemical change!)
…so shine in different directions (so pump pulse doesn’t ruin your light detector)
Pump beam travels across width of cell (so ensure uniform illumination). Probe beam travels along length of cell (increase signal)
Sample cell
Pump
Probe
Light 1
Light 2
Light detector
Eg
Photodiode
Timing
electronics

## Slide 29: Laser ablation of nanoparticles
https://youtu.be/m_ScOUNAdlM?t=101
Background context

## Slide 30: Laser ablation of nanoparticles
Lam, J., Lombard, J., Dujardin, C., Ledoux, G., Merabia, S., & Amans, D. (2016). Dynamical study of bubble expansion following laser ablation in liquids. Applied Physics Letters, 108(7), 074104.
Background context

## Slide 31: Changing probe wavelength
Probe can be white (or, in general, “polychromatic”) - contains a mixture of different wavelengths.
…or can be monochromatic: all the light has the same wavelength, usually: absorption by a species of interest.
Wavelength
Intensity
Wavelength
Intensity
Spectrum of intermediate

## Slide 32: Using white light as the probe
White light can be split up using a prism or diffraction grating.
The light can then be detected with an array of detectors, to give a spectrum.
Alternatively, you can use a “monochromator” with a single detector, to pick a single wavelength at a time.
Probe beam of white light
Sample

## Slide 33: Pump and probe lasers
Pump and probe are usually different lasers / light sources.
  Pump has to be intense but exact wavelength less important; probe has to be “tunable” so you can vary the wavelength to probe the specific species that you want to look at
Can have pulse and probe from same laser (see later slide)
Each pump pulse usually only makes a small fraction of (pre-) reactant react, so probe only detects a very small signal. The reaction can therefore be repeated many times, adding all of the probe data, to increase the signal.

## Slide 34: Probe Timing
Option 1: Timing of probe light is
  On continuously (detector system records absorption throughout reaction; triggered by pump pulse)
  Real-time data acquired through a computer. (Note: maximum computer speed – we can only study phenomena as fast as we can save the data)

## Slide 35: Continuous Laser Absorption
Absorption of probe by unstable reactant
Time
Reactive species disappears through reaction
Probe wavelength set to absorption by reactant (generated by pump)
Absorption of probe by intermediate
Time
Intermediate appears then disappears
Probe wavelength set to absorption by intermediate
Pump
pulse
Pump
pulse

## Slide 36: Probe Timing
Option 2: Timing of probe light may be
  Pulsed, with a fixed delay after the pump pulse. (You repeat the experiment varying the delay)
  Data acquired continuously

## Slide 37: Pulsed laser absorption
Absorption of probe by unstable reactant
Time
Probe wavelength set to absorption by reactant
Pump
pulse
Absorption of probe by intermediate
Time
(2) Probe wavelength set to absorption by intermediate
Variable delay
Probe
pulse
Variable delay
Probe
pulse
Pump
pulse

## Slide 38: Using the same light source
White light generation
x
Mono-chromatic pump beam
White probe beam
Eg. If x = 15cm = 0.15m
Probe pulse travels 2x
= 0.3m further than pump pulse.
It therefore arrives at the sample
0.3 / (3 x 108 ms-1) = 1ns later than the pump pulse. (Time = distance / speed)

## Slide 39: Learning outcomes
Today we have: Reviewed various methods for measuring kinetics in real experiments Described methods for in situ monitoring Described methods for measuring very fast kinetics processes.

## Slide 40: And in summary
During this lecture course we have covered:
Multi-step kinetics
Steady-state approximation
Chain reactions
Branching reactions and explosions
Practical kinetics